## Slide 1: Problem Statement Motivation & Introduction
Prediction of fluid injection characteristics (e.g., injectivity) from geophysical data (e.g., micro-seismicity) is essential to a suite of energy-related applications such as geothermal energy recovery and carbon sequestration.
Micro-seismicity data consist of the record of micro-seismic events (i.e., small earthquakes) that occur during and following injection. The data provide the location and magnitude of micro-earthquakes.
There are available datasets from field-scale “experiments” that include both micro-seismicity and injection data. One example is data collected in DOE EGS-Collab Project.

## Slide 2: DOE EGS Collab Project
(b)
Injector-Producer + Instrumentation
Data for Injection Episodes – #1 - #5
[Schoenball et al., 2020]

## Slide 3: ML Problem Statement Formulation
Predict the evolution of ‘injectivity’ defined as the ratio of ‘injection rate’ and ‘pressure’ , i.e. = / , given micro-earthquake MEQ magnitudes and locations over time .
Input*:
* Other features of micro-earthquakes may be included.
Output:
where are the fixed coordinates of ‘injection well’

## Slide 4: Physics-Informed ML ? Formulation
Predict the evolution of ‘injectivity’ defined as the ratio of ‘injection rate’ and ‘pressure’ , i.e. = / , given micro-earthquake MEQ magnitudes and locations over time .
Input*:
* Other features of micro-earthquakes may be included.
Output: from which may be estimated (Darcy’s law)
Empirical Physics law: (can we learn & ?)